Richard Aviles
11/21/17

Wireshark 7

1) 30 Munroe St
    linksys12

2) 0.1024 seconds for both.

3) 00:16:b6:f7:1d:51

4) ff:ff:ff:ff:ff:ff

5) 00:16:b6:f7:1d:51

6) Four data rates: 1(B), 2(B), 5.5(B), 11(B), [Mbit/sec]
Eight extended supported rates: 6(B), 9, 12(B), 18, 24(B), 36, 48, 54, [Mbit/sec]

7) Source: 00:13:02:d1:b6:4f
Destination: 00:16:b6:f4:eb:a8
BSS Id: 00:16:b6:f7:1d:51
The MAC address for the host is the source. The access point and first-hop router is the destination.
The address of the host sending the TCP segment is 192.168.1.109. The address of the destination is 128.119.245.12. The destination address corresponds to the destination server gaia.cs.umass.edu.

8) Source: 00:16:b6:f4:eb:a8
Destination: 91:2a:b0:49:b6:4f
BSS Id: 00:16:b6:f7:1d:51
The MAC address for the host is the destination. The access point and first-hop router is the source.
No the sender MAC address in the frame does not correspond to the IP address of the device that sent the TCP segment.

9) A DHCP release and a Deauthentication is sent. We might have expected to see a Disassociation as well even though it was not present.

10) 6 Authentication frames are sent.

11) Yes the host does want the authentication to require to be opened.

12) I do not see an Authentication from the linksys in the trace.

13) At t = 63.168087 the host sends an Authentication and at t = 63.169071 the AP sent one back to the host.

14) The associate request was sent at t = 63.169910. The associate response was sent at t = 63.192101.

15) The host is willing to use transmission rates 1(B), 2(B), 5.5(B), 11(B), 6(B), 9, 12(B), 18, 24(B), 36, 48, 54, [Mbit/sec]. The AP is willing to use the same transmission rates.

16) Probe Request:
Source: 00:12:f0:1f:57:13
Destination: ff:ff:ff:ff:ff:ff
BSS Id: ff:ff:ff:ff:ff:ff

Probe Response:
Source: 00:16:b6:f7:1d:51
Destination: 00:12:f0:1f:57:13
BSS Id: 00:16:b6:f7:1d:51

The probe request is used to find an AP. The probe response is sent by the AP to the host.